ECE 2030b, Intro. To Computer Eng., HW-2  (was 2001 QUIZ 1)

Due  Sept. 13, 2002

Question 1 – Truth Table.

Given the Boolean expression:  Out =  AB  +  ABC   +  A’B’

Hint – simplify first ________________________

Complete the truth table.

| A | B | C | Out |
| --- | --- | --- | --- |
| 0 | 0 | 0 |  |
| 0 | 0 | 1 |  |
| 0 | 1 | 0 |  |
| 0 | 1 | 1 |  |
| 1 | 0 | 0 |  |
| 1 | 0 | 1 |  |
| 1 | 1 | 0 |  |
| 1 | 1 | 1 |  |

Question 2 – CMOS Logic

Draw the CMOS  transistor diagram for AB + CD.  Assume A, A’, B, B’, C, C’,D’ and D’ signals are available.

# Question 3 – Logic Identities                Simplify the follow Boolean expressions:

A.  X(X+Y)

B.  X + Y + XZ

C.   (X’ + Y’)’

- X + XY

XY + YZ +  X’Z

- Question 4 – Minterm and Maxterm Indices

For the truth tables below, express the minterm sum of products, and the maxterm product of sums:

| A | B | C | F |
| --- | --- | --- | --- |
| 0 | 0 | 0 | 0 |
| 0 | 0 | 1 | 0 |
| 0 | 1 | 0 | 1 |
| 0 | 1 | 1 | 0 |
| 1 | 0 | 0 | 0 |
| 1 | 0 | 1 | 1 |
| 1 | 1 | 0 | 0 |
| 1 | 1 | 1 | 1 |

sum of products  ____________________________________________________________________

product of sums  ____________________________________________________________________

Draw a Karnaugh Map for the truth table in Question 4. Circle the Prime Implicants with a solid line.  Label the Essential prime Implicants with a dashed line.

| A \ BC |  |  |  |  |
| --- | --- | --- | --- | --- |

Question 5 – Karnaugh Map    For the Karnaugh map below, circle the Prime Implicants and label the Essential Prime Implicants with “EPI”.

| AB \ CD | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 00 | 0 | 1 | 1 | 0 |
| 01 | 1 | 0 | 1 | 1 |
| 11 | 0 | 0 | 0 | 1 |
| 01 | 0 | 1 | 1 | 0 |

Write the reduced logic expression: ____________________________________________

maxterm indices (decimal) ____________________________________________________

# Text boxes

# Out