Transistor-Level Circuit Understanding

For the following switch level circuit, complete the truth table computed. If a  floating or shorted output is detected, indicate that in the truth table. If no floats or shorts are detected, write the Boolean expression computed by the circuit.

| A | B | C | Out |
| --- | --- | --- | --- |
| 0 | 0 | 0 | 1 |
| 0 | 0 | 1 | 1 |
| 0 | 1 | 0 | 0 |
| 0 | 1 | 1 | 0 |
| 1 | 0 | 0 | 1 |
| 1 | 0 | 1 | 1 |
| 1 | 1 | 0 | 0 |
| 1 | 1 | 1 | 1 |

“Out”  is  “1”  if  B is “0” or A’ and C’ are both “0”.

Write the Boolean expression for this function,  Out  =  B’ + A’C’

Given the Boolean expression:  Out =  A’C + ABC  = C( A’+AB) = C(A’+B)

(if logic expression is not simplified, there should be 10 FET’s below)

Complete the truth table.

| A | B | C | Out | Note |
| --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 |  |
| 0 | 0 | 1 | 1 | A’C=1 |
| 0 | 1 | 0 | 0 |  |
| 0 | 1 | 1 | 1 | A’C=1 |
| 1 | 0 | 0 | 0 |  |
| 1 | 0 | 1 | 0 |  |
| 1 | 1 | 0 | 0 |  |
| 1 | 1 | 1 | 1 | ABC = 1 |

Draw the CMOS  transistor diagram.  Assume A, A’, B, B’, C, C’ signals are available.

Given the truth table.

| A | B | C | Out |
| --- | --- | --- | --- |
| 0 | 0 | 0 | 0 |
| 0 | 0 | 1 | 0 |
| 0 | 1 | 0 | 0 |
| 0 | 1 | 1 | 1 |
| 1 | 0 | 0 | 0 |
| 1 | 0 | 1 | 1 |
| 1 | 1 | 0 | 1 |
| 1 | 1 | 1 | 1 |

Write the Boolean expression as 3 terms:  Out =  AB +BC + AC  from observation that Out is “1” whenever any two inputs are one).

By the minterm approach:    	Out = A’BC +AB’C + ABC’ + ABC

Using Boolean Equalities:    A’BC + ABC = BC    and  ABC = ABC + ABC +ABC

OUT = AB + BC + AC

Draw the CMOS  transistor diagram.  Assume A, A’, B, B’, C, C’ signals are available.

Bonus – use a Karnaugh map to find the simplest logic expression for Problem 3.  There are three Essential Prime Implements, AC (blue), BC (green), and AB (red).

| A \ BC | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 1 | 0 |
| 1 | 0 | 1 | 1 | 1 |

# Text boxes

A

A

B''

B''

C''

C''

# Out

# Out

A

A

B'

C’

B'

# Out

### A’

### B’

### C’

### A’

### C’

### B’

### B’

### A’

### B’

### C’

### A’

### C’