Given the Boolean expression:  Out =  BC’+ ABC

Complete the truth table.

| A | B | C | Out |
| --- | --- | --- | --- |
| 0 | 0 | 0 |  |
| 0 | 0 | 1 |  |
| 0 | 1 | 0 |  |
| 0 | 1 | 1 |  |
| 1 | 0 | 0 |  |
| 1 | 0 | 1 |  |
| 1 | 1 | 0 |  |
| 1 | 1 | 1 |  |

Draw the CMOS  transistor diagram.  Assume A, A’, B, B’, C, C’ signals are available. Use only three p-mos and three  n-mos transistors

Given the truth table.

| A | B | C | Out |
| --- | --- | --- | --- |
| 0 | 0 | 0 | 1 |
| 0 | 0 | 1 | 1 |
| 0 | 1 | 0 | 1 |
| 0 | 1 | 1 | 0 |
| 1 | 0 | 0 | 1 |
| 1 | 0 | 1 | 0 |
| 1 | 1 | 0 | 0 |
| 1 | 1 | 1 | 0 |

Write the Boolean expression as 3 terms:  Out =

Draw the CMOS  transistor diagram.  Assume A, A’, B, B’, C, C’ signals are available.

Bonus – use a Karnaugh map to find the simplest logic expression for Problem 3.  There are three Essential Prime Implements.

| A \ BC | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 0 | 1 | 1 | 0 | 1 |
| 1 | 1 | 0 | 0 | 0 |

# Text boxes

# Out

# Out